## Slide 1: DDH networks Case study 2025
Presentation by
Darren D Huynh

## Slide 2: Objectives
Presentation by
Darren D Huynh
Discuss VLSM Scheme and Logical Topology
Configure OSPFv2 and RIP for routing
Configure GRE and Secure GRE Tunnel with IPsec
Discuss NAT and Germany ACL
DHCP and VLAN Configurations
Verification and Testing
Questions

## Slide 3: PHASE 1: LAN/WAN and INTERFACES

## Slide 4
COLORADO
LIMA
BELGUM
GERMANY

## Slide 5: VLSM SCHEME
IP ADDRESS | SUBNET | CIDR | ACTIVE | NAME | REQUIRED HOST
172.26.0.0 | 255.255.252.0 | /22 | YES | GERMANY | 512
172.26.4.0 | 255.255.255.0 | /24 | YES | COLORADO VLAN 100 | 250
172.26.5.0 | 255.255.255.0 | /24 | YES | COLORADO VLAN 200 | 250
172.26.6.0 | 255.255.255.0 | /24 | YES | COLORADO VLAN 300 | 250
172.26.7.0 | 255.255.255.192 | /26 | YES | LIMA | 50
172.26.255.236 | 255.255.255.252 | /30 | YES | SYSLOG SERVER | 2
172.26.255.240 | 255.255.255.252 | /30 | YES | SNMP SERVER | 2
172.26.255.244 | 255.255.255.252 | /30 | YES | MANAGEMENT | 2
172.26.255.248 | 255.255.255.252 | /30 | YES | LINK to COLORADO | 2
172.26.255.252 | 255.255.255.252 | /30 | YES | LINK to LIMA | 2
209.165.100.0 | 255.255.255.252 | /30 | YES | GERMANY to ISP | 2
209.165.200.0 | 255.255.255.252 | /30 | YES | COLORADO to ISP | 2

## Slide 6: LOGICAL TOPOLOGY

## Slide 7: COLORADO INTERFACES
ROUTER | INTERFACES | IP ADDRESS | CIDR | CONNECTION TYPE | ACTIVE | DESCRIPTION
COLORADO | G0/0/1 | N/A | N/A | ETHERNET | YES | LINK to COLO-LAN
COLORADO | G0/0/1.100 | 172.26.4.1 | /24 | ENCAPSULATED | YES | LINK to VLAN 100
COLORADO | G0/0/1.200 | 172.26.5.1 | /24 | ENCAPSULATED | YES | LINK to VLAN 200
COLORADO | G0/0/1.300 | 172.26.6.1 | /24 | ENCAPSULATED | YES | LINK to VLAN 300
COLORADO | G0/0/1.401 | 172.26.255.245 | /30 | ENCAPSULATED | YES | LINK to VLAN 401
COLORADO | S0/1/0 | 209.165.200.1 | /30 | SERIAL | YES | LINK to ISP
COLORADO | S0/1/1 | 172.26.255.250 | /30 | SERIAL | YES | LINK to BELGUM
COLORADO | Tunnel0 | 1.1.1.1 | /30 | TUNNEL | YES | TUNNEL to GERMANY
COLORADO | Lo0 | 10.10.10.10 | /32 | LOOPBACK | YES | LOOPBACK for COLORADO

## Slide 8: GERMANY INTERFACES
ROUTER | INTERFACES | IP ADDRESS | CIDR | CONNECTION TYPE | ACTIVE | DESCRIPTION
GERMANY | G0/0/0 | 172.26.0.0 | /22 | ETHERNET | YES | LINK to GERMANY-LAN
GERMANY | S0/1/0 | 209.165.100.2 | /30 | SERIAL | YES | LINK to ISP
GERMANY | Tunnel0 | 1.1.1.2 | /30 | TUNNEL/SERIAL | YES | TUNNEL to COLORADO

## Slide 9: LIMA INTERFACES
ROUTER | INTERFACES | IP ADDRESS | CIDR | CONNECTION TYPE | ACTIVE | DESCRIPTION
LIMA | G0/0/0 | 172.26.7.1 | /26 | ETHERNET | YES | LINK to LIMA-LAN
LIMA | S0/1/0 | 172.26.255.254 | /30 | SERIAL | YES | LINK to BELGUM
LIMA | Lo0 | 30.30.30.30 | /32 | LOOPBACK | YES | LOOPBACK for LIMA

## Slide 10: BELGUM INTERFACES
ROUTER | INTERFACES | IP ADDRESS | CIDR NOTATION | CONNECTION TYPE | ACTIVE | DESCRIPTION
BELGUM | G0/0/0 | 172.26.255.237 | /30 | ETHERNET | YES | LINK to SYSLOG
BELGUM | G0/0/1 | 172.26.255.241 | /30 | ETHERNET | YES | LINK to SNMP
BELGUM | S0/1/0 | 172.26.255.249 | /30 | SERIAL | YES | LINK to COLORADO
BELGUM | S0/1/1 | 172.26.255.253 | /30 | SERIAL | YES | LINK to LIMA
BELGUM | Lo0 | 20.20.20.20 | /32 | LOOPBACK | YES | LOOPBACK for BELGUM

## Slide 11: PHASE 2: OSPFv2 and Ripv2

## Slide 12: OSPFv2 and ripv2
COLORADO
GERMANY

## Slide 13: OSPFv2 and ripv2
BELGUM
LIMA

## Slide 14: PHASE 3: CONFIGURATIONS

## Slide 15: NAT with pat Configs

## Slide 16: NAT with pat Configs

## Slide 17: GRE TUNNEL

## Slide 18: IPsec Configs
ISAKMP POLICY
TRANSFORM SET
COLORADO KEY
GERMANY KEY
COLO CRYPTO MAP
GERMANY CRYPTO MAP

## Slide 19: IPsec Configs

## Slide 20: GERMANY ACL

## Slide 21: PHASE 3: DHCP AND VLAN

## Slide 22: DHCP POOLS
POOL | NETWORK | SUBNET | EXCLUDED-ADDRESS | ADDRESS RANGE | DOMAIN NAME | DEFAULT ROUTER
COLO VLAN 100 | 172.26.4.0 | /24 | 172.26.4.1-.10 | 172.26.4.11-254 | COLO.com | 172.26.4.1
COLO VLAN 200 | 172.26.5.0 | /24 | 172.26.5.1-.10 | 172.26.5.11-.254 | COLO.com | 172.26.5.1
COLO VLAN 300 | 172.26.6.0 | /24 | 172.26.6.1-.10 | 172.26.6.11-.254 | COLO.com | 172.26.6.1
GERMANY | 172.26.0.0 | /22 | 172.26.0.1-.20 | 172.26.0.21 - 172.26.3.254 | GERM.com | 172.26.0.1
LIMA | 172.26.7.0 | /26 | 172.26.7.1-.10 | 172.26.7.11-.254 | LIMA.com | 172.26.7.1

## Slide 23: DHCP CONFIGS

## Slide 24: VLANs
MANAGEMENT VLAN: 192.168.255.246

## Slide 25: PHASE 4: TESTING AND VERIFICATION

## Slide 26: TESTING AND VERIFICATION
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
Host on VLAN1 | ISP | HTTP | PASS
Host on VLAN1 | Host on Germany LAN | ICMP | PASS
Host on VLAN1 | Host on VLAN 2 | ICMP | PASS
Host on VLAN1 | Host on VLAN 3 | ICMP | PASS
Host on VLAN 2 | Host on VLAN 3 | ICMP | PASS
Host on VLAN 2 | Host on Germany LAN | ICMP | PASS
Host on VLAN 2 | ISP | HTTP | PASS
Host on VLAN 3 | Host on Germany LAN | ICMP | PASS
Host on VLAN 3 | ISP | HTTP | PASS
Host on Germany | ISP | HTTP | PASS
Host on Germany | ISP | Telnet | FAIL
Router on Colorado | SYSLog Server | LOGS | PASS
NAT on Germany |  | NAT | PASS
NAT on Colorado |  | NAT | PASS
NAT on ISP | ISP | WEB | PASS
TELNET | ISP | TELNET | FAIL

## Slide 27: NAT VERIFICAITON

## Slide 28: IPsec Verification

## Slide 29: IPsec Verification

## Slide 30: GERMANY VERIFICATION
SOURCE | DESTINATION | PROTOCOL | RESULT
Host on Germany | ISP | ICMP | FAIL
Host on Germany | ISP | HTTP | PASS
Host on Germany | LIMA | ICMP | PASS
Host on Germany | SNMP | ICMP | PASS
Host on Germany | SYSLOG | ICMP | PASS
Host on Germany | VLAN 100 | ICMP | PASS
Host on Germany | VLAN 200 | ICMP | PASS
Host on Germany | VLAN 300 | ICMP | PASS

## Slide 31: GERMANY VERIFICATION

## Slide 32: GERMANY VERIFICATION

## Slide 33: Colorado VLAN 100 verification
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
VLAN 100 | ISP | HTTP | PASS
VLAN 100 | LIMA | ICMP | PASS
VLAN 100 | SNMP | ICMP | PASS
VLAN 100 | SYSLOG | ICMP | PASS
VLAN 100 | GERMANY | ICMP | PASS
VLAN 100 | VLAN 200 | ICMP | PASS
VLAN 100 | VLAN 300 | ICMP | PASS

## Slide 34: Colorado VLAN 100 verification

## Slide 35: Colorado VLAN 200 verification
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
VLAN 200 | ISP | HTTP | PASS
VLAN 200 | LIMA | ICMP | PASS
VLAN 200 | SNMP | ICMP | PASS
VLAN 200 | SYSLOG | ICMP | PASS
VLAN 200 | GERMANY | ICMP | PASS
VLAN 200 | VLAN 100 | ICMP | PASS
VLAN 200 | VLAN 300 | ICMP | PASS

## Slide 36: Colorado VLAN 200 verification

## Slide 37: Colorado VLAN 300 verification
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
VLAN 300 | ISP | HTTP | PASS
VLAN 300 | LIMA | ICMP | PASS
VLAN 300 | SNMP | ICMP | PASS
VLAN 300 | SYSLOG | ICMP | PASS
VLAN 300 | GERMANY | ICMP | PASS
VLAN 300 | VLAN 100 | ICMP | PASS
VLAN 300 | VLAN 200 | ICMP | PASS

## Slide 38: Colorado VLAN 300 verification

## Slide 39: LIMA verification
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
Host on LIMA | ISP | HTTP | PASS
Host on LIMA | GERMANY | ICMP | PASS
Host on LIMA | SNMP | ICMP | PASS
Host on LIMA | SYSLOG | ICMP | PASS
Host on LIMA | VLAN 100 | ICMP | PASS
Host on LIMA | VLAN 200 | ICMP | PASS
Host on LIMA | VLAN 300 | ICMP | PASS

## Slide 40: LIMA verification

## Slide 41: BELGUM verification
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
SYSLOG | ISP | HTTP | PASS
SYSLOG | GERMANY | ICMP | PASS
SYSLOG | LIMA | ICMP | PASS
SYSLOG | SNMP | ICMP | PASS
SYSLOG | VLAN 100 | ICMP | PASS
SYSLOG | VLAN 200 | ICMP | PASS
SYSLOG | VLAN 300 | ICMP | PASS
SOURCE | DESTINATION | PROTOCOL | EXPECTED RESULT
SNMP | ISP | HTTP | PASS
SNMP | GERMANY | ICMP | PASS
SNMP | LIMA | ICMP | PASS
SNMP | SYSLOG | ICMP | PASS
SNMP | VLAN 100 | ICMP | PASS
SNMP | VLAN 200 | ICMP | PASS
SNMP | VLAN 300 | ICMP | PASS

## Slide 42: BELGUM verification (SYSLOG)

## Slide 43: SYSLOG VERIFICAITON

## Slide 44: BELGUM verification (SNMP)

## Slide 45: SNMP VERIFICAITON

## Slide 47: Thank you
Darren Huynh